## Slide 1: MMRI Health and Safety Awareness
Revised August 2025
Brady Semple

## Slide 2: Introductions
Key Staff
  Dr. Stephen Veldhuis – Director, MPAL
  Steve Remilli – Operations Manager
  Brady Semple – Facilities Manager
  Ellen Mack– Institute Administrator

## Slide 3: Laboratories
The MMRI has several different lab areas:
  Machine Shop (MMRI 111)
    Contains mills, lathes, microscopes, and general machining and fabrication equipment
  Waterjet Room (MMRI 109)
    Waterjet and welding, grinding, and sandblasting equipment
  Materials Property Assessment Laboratory (MMRI 108)
    Surface test equipment: indenters, AFM, tribometers, and scratch testers
  PVD Coater Lab (MMRI 215)
    PVD coater, laser cutter, and associated equipment

## Slide 4: MMRI Health and Safety
Objectives
  To establish a safe and enjoyable working environment for students, staff, faculty, and guests
  To highlight existing documentation available through the Ontario Occupational Health and Safety Act (OHSA) and McMaster University Health and Safety (UHS) - all information presented comes from these sources
  To prevent situations that may result in personal injury or death

## Slide 5: MMRI Health and Safety
Both supervisors and workers are required to enforce and abide by safe working practices as they have been laid out in this and other training documents. This includes safe and proper use of PPE and all equipment
Maximum fines for corporations are $500,000
Maximum fines for individuals are $25,000 and imprisonment for up to 12 months

## Slide 6: MMRI Health and Safety
Key Terminology
  Worker: A person who works or provides service for monetary compensation
  Employer: A person who employs or contracts for the service of others
  Supervisor: A person who has control of a workplace or authority over a worker
  PPE: Personal Protective Equipment (e.g., safety glasses, shoes, goggles)
  SOP: Standard Operating Procedure
  WHMIS: Workplace Hazardous Material Information System
  SDS: Safety Data Sheet
  UHS: University Health and Safety (formerly EOHSS)
  JHSC: Joint Health and Safety Committee
  MOL: Ministry of Labour

## Slide 7: MMRI Health and Safety
Joint Health and Safety Committee (JHSC)
  A tool which workers and management can use to work together to participate in safety discussions and improvement
  Acts in an advisory role to encourage awareness and compliance
  Undertakes audits and inspections
The MMRI is a member of the MARC JHSC
  Any safety concerns can be raised with our JHSC by contacting Brady Semple (semplebg@mcmaster.ca)
  Or reach out to any other members of the committee : https://hr.mcmaster.ca/app/uploads/2019/01/JHSC-Master-List.pdf

## Slide 8: MMRI Health and Safety
Rights of the Worker
  Right to Know:
    As a worker, you have the right to be informed by the employer of known or likely hazards in the workplace, and to be provided with the information, instructions, education, training, and supervision necessary to protect your health and safety
  Right to Participate:
    Workers are allowed to have input on the steps taken by the employer to ensure health and safety. This includes participating in the JHSC, reporting concerns that could affect the health and safety or yourself or your coworkers, and making suggestions to your committee or employer
  Right to Refuse:
    You have the right to refuse work that could affect your health and safety and that of others. The right to refuse is normally used when the first two rights fail to ensure your health and safety. Exercising this right is serious and should not be done lightly or as a routine method of solving workplace problems

## Slide 9: MMRI Health and Safety
McMaster Policies and Programs
  Ministry of Labour – Ontario Wide
  Central Health and Safety Committee – Campus Wide
  Faculty Health and Safety – Engineering Specific
  MARC Health and Safety Committee – Only the MARC building and the MMRI

## Slide 10: MMRI Health and Safety
Risk Management Manuals/Policies
McMaster University Health and Safety
  UHS has developed a ranges of standardized operating policies and procedures for use campus wide
  Copies of the policies can be found on the UHS website: https://hr.mcmaster.ca/employees/health_safety_well-being/our-safety/risk-management-manuals-rmms/
The Ontario Occupational Health and Safety Act
  OHSA provides additional regulations that are to be followed in the workplace

## Slide 11: MMRI Health and Safety
Incident Reporting
  Any accidents or incidents in the workplace involving injuries or potential hazards must be reported to your supervisor immediately
  McMaster Incident Reporting Form:
  https://hr.mcmaster.ca/app/uploads/2018/11/injury-incident-report-fillable-1-36.pdf

## Slide 12: MMRI Health and Safety
Incident Reporting
  Employee Responsibilities:
    Promptly receive appropriate medical treatment. At MIP, Dial 911 for emergency response
    Notify your supervisor as soon as possible of injury and any related healthcare measures taken
    Assist with the completion of an injury/incident form and sign it
    Assist in the incident investigation and implementation of any corrective action
    Adhere to the legal requirements of WSIB and participate in McMaster University’s Return to Work Program if modified work and/or lost time results from a work-related injury

## Slide 13: MMRI Health and Safety
“Critical Injury” is an injury of a serious nature that includes any of the following:
  Places life in jeopardy
  Produces unconsciousness
  Results in substantial loss of blood
  Involves the fracture of an arm or leg
  Involves the amputation of an arm, hand, leg, or foot
  Consists of burns to a major portion of the body
  Causes the loss of sight on an eye
In the case of a critical injury, supervisors are responsible for:
  Securing the accident site to ensure that further injury is prevented
  Immediately arranging for medical and emergency assistance by calling Security at “88” or “5555” at host hospitals and “911” at any other off-campus locations
  Immediately notifying Environmental and Occupational Health Support Services at 905-525-9140x24352 and communicating details of the incident
  Ensuring that the site remains undisturbed until Environmental and Occupational Health Support Services provide clearance
  Cooperating with directives from Environmental and Occupational Health Support Services and the Ministry of Labour

## Slide 14: MMRI Health and Safety
McMaster has a range of standard safety courses that MUST be completed before you can begin to work at the MMRI.
A training matrix developed by UHS is available here: https://hr.mcmaster.ca/app/uploads/2019/02/Corporate-Training-Matrix.pdf
Sign up for required training through Mosaic (https://mosaic.mcmaster.ca/)
A summary of the MMRI relevant courses is presented here:
Mandatory For Everyone: | MMRI Required: | Equipment/Role Specific
SAFE Training Health & Safety Orientation​ Violence & Harassment Prevention​ WHMIS 2015​ | Chemical Handling and Spills​ Ladder Safety​ Machine Guarding Awareness​ Noise Awareness | Gas Cylinder (welding and coater)​ Laser Safety (laser cutter)​ Lock-Out/Tag-Out (maintaining equipment)​ Fire Warden (Brady, Kevin, Dr. Veldhuis, Michelle)​ Accident Investigation (supervisors)​ Due Diligence (supervisors)

## Slide 15: Working in the MMRI – General Safety
Emergencies
  In the event of an emergency, call 911
    Our location is 230 Longwood Road South, Hamilton, Ontario
  If time and the incident conditions permit, follow up with a call to McMaster security through either:
    Telephone: 905-525-9140 x24281
    The McMaster Security App

## Slide 16: Working in the MMRI – General Safety
Fire Safety
  When an alarm sounds, secure equipment in a safe condition and leave the building by the nearest exit immediately
  Do not use elevators
  Feel doors before opening them. If hot, find a different exit
  Close all doors behind you as you evacuate
  If it is unsafe to evacuate, close doors and block cracks with a damp towel. Call 911 immediately
  Do not re-enter building until given an explicit all-clear by a fire warden, fire department, or security
  *If you require any special accommodations in order to evacuate the building safely, discuss them in advance with your supervisor

## Slide 17: Working in the MMRI – General Safety
Fire Safety – Muster Point
  When evacuating the building, leave via the nearest exit
  Make your way around the building to the MMRI’s muster point: Across the road from the MMRI main entrance, West of the building

## Slide 18: Working in the MMRI – General Safety
Safety Data Sheets (SDS):
  McMaster has moved to using an online SDS system
  SDS sheets can be found here: https://jr.chemwatch.net/chemwatch.web/account/autologinbyip (no sign in required if logging in from campus)
  A lab laptop in the SouthWest corner of the Machine Shop has a link to this address on the desktop
  If you are bringing any chemicals into the laboratory that are not found in this SDS listing, let your supervisor know before bringing it into the lab

## Slide 19: Working in the MMRI – General Safety
Hazardous Waste Disposal
  All chemical waste must be handled properly, not dumped down drains
  For solvents, disposal containers are available in MPAL
  For waste oil and machine coolant, there are disposal bins in the Machine Shop
  If either container is full, let your supervisor know so that it can be emptied
  If you have any special waste to dispose of, let your supervisor know

## Slide 20: Working in the MMRI – General Safety
Only operate equipment that you have been trained and approved to use by your supervisor
  If you have any questions, concerns, or doubts, ask your supervisor for help
Alteration to machines and equipment is prohibited without specific authorization
Floors, walkways, and work areas should be kept clean, clear, and tidy at all times
Spills and damage to equipment must be reported immediately to your supervisor
Never leave equipment running unattended without explicit permission

## Slide 21: Working in the MMRI – General Safety
Hours of Operation
  The MMRI operates on weekdays (excluding days when the university is closed)
  8:30 AM until 5:00 PM
    Stop operating equipment by 4:30 PM in order to give enough time to clean up before end-of-day
If special circumstances require that you work on any equipment in the MMRI outside of these hours, inform your supervisor so that arrangements can be made
  McMaster has Working Alone policies that dictate the University’s process: https://hr.mcmaster.ca/app/uploads/2022/05/RMM-304-Working-Alone-Program.pdf
  When operating machinery, another member of the MMRI must be present

## Slide 22: Working in the MMRI – General Safety
Electrical
  Use extension cords only when necessary
  Extension cords should never be used for stationary/permanent purposes
  If you find a cord in poor condition, make your supervisor aware of it immediately. Do not use it
    Your supervisor will repair or dispose of the cord in question
  Mark and tape down all extension cords as necessary
  Do not alter or repair electrical equipment unless authorized to do so
  Abide by lock-out tag-out procedures when working on equipment

## Slide 23: Working in the MMRI – General Safety
Consequences
  Failure to follow the rules and policies outlined in this and other safety training will result in a warning and expulsion from the lab until the safety issue can be remedied
  Repeated offense will result in a written notice to the offender and their supervisor
  If an offender shows a repeated disregard for or inability to follow safety requirements, then they will be banned from the lab environment

## Slide 24: Working in the MMRI – General Safety
General Attire in lab spaces
  Closed-toe shoes
  Full-length pants
  No watches, rings, necklaces, or loose clothing – this can get caught in machinery and pose a serious risk
  Long hair should be tied back and/or tucked in to reduce risk

## Slide 25: Working in the MMRI
Headphones
  No headphones or earbuds are allowed to be worn in the MMRI except in the desk areas
  They reduce your awareness of what is going on around you, and make it difficult for your coworkers and supervisor to alert you of hazards
  While headphones can reduce the perceived volume of sounds around you, they are not hearing protection, and the music played through them adds to the noise level you are experiencing

## Slide 26: Working in the MMRI
PPE
  Safety glasses and safety shoes must be worn in the:
    Waterjet Lab
    Machine Shop – Any point within the yellow lines on the floor
  Safety glasses and shoes must be CAS approved designs
    Shoes will have a green triangle indicating such
  Additional PPE requirements depending on the task at hand:
    Hearing protection (always required in waterjet room when waterjet is running)
    Gloves (when handling material but NEVER when working on machinery with rotating components)
    As needed (discuss with staff to arrange special PPE to be supplied)

## Slide 27: Working in the MMRI
PPE
  MPAL
    Safety Shoes – recommended but not required
    Safety Glasses – recommended but not required
    Gloves (Nitrile) – required with AFM, indenters, microscope turrets. Recommended with all equipment and samples
  Coater Lab
    Safety Glasses – when working in coating chamber
    Safety Shoes – when performing maintenance or replacing parts
    Gloves – when working in coating chamber

## Slide 28: Working in the MMRI
PPE – Special Events
  Tours:
    It may be necessary to have a tour group through the lab where not all members of the tour have complete PPE
    If this is the case:
      Provide everyone with safety glasses from the rack at the front (West) of the lab
      Warn people within the lab that a tour is coming through
      Escort the members of the tour, do not allow them to roam freely
      Make sure that all material handling activities (cranes, forklifts, pallet trucks, etc.) are kept well away from the tour
      You are responsible for the members of the tour group
  Events:
    Very rarely, special events like an open house may allow PPE requirements to be fully relaxed. Your supervisor will communicate this well in advance

## Slide 29: Working in the MMRI
Material Handling
  Material handling is a common source of injury
  For heavy materials, ask a staff member for help to use an overhead crane or forklift for you
  Be aware of sharp edges and corners. Use gloves to protect your hands from cuts and scrapes
  Be careful when stacking material. Do not make unstable stacks, and secure loads properly

## Slide 30: Working in the MMRI
Cut Hazards
  Many of the materials in the machine shop are inherently sharp. Tooling and workpieces in particular pose risks
  Knives, scissors, deburring tools, and other hand-held cutting edges are also frequently used in the labs. Handle with caution, and never draw a knife or other cutting tool towards your hands or body
  Do not run fingers along edges of workpieces, especially if they have not been thoroughly de-burred
  Be careful when handling cutting tools, especially if oily (such as when removing them from a machine)
  If you drop something sharp, move your feet out of the way and do not attempt to catch it. Allow it to fall to the floor

## Slide 31: Working in the MMRI
Compressed Air
  Compressed air is present throughout the lab space in various hoses and plumbing
  Be aware that compressed air represents an enormous store of energy
  No not modify, adjust, or otherwise handle compressed air line or systems without specific permission from your supervisor
  Make sure not to allow air lines to run across walkways or aisles
  Do not use compressed air to clean yourself, your clothing, or any other person. Compressed air pointed at your skin is a serious potential danger
  Avoid using compressed air to clean machinery except where absolutely necessary

## Slide 32: Working in the MMRI
Clean-up
  Be sure to clean your workstation at the end of every day
  This includes:
    Putting tools away
    Cleaning and wiping down surfaces
    Disposing of rags or any other waste
    Labeling samples and tooling and storing them in project boxes
      Make sure samples and sample boxes are clearly labelled with your name and the project code
  At the end of the job, fully clean off the equipment
    Remove any special fixturing and workpieces
    Break down tooling assemblies and put away
    Put away any data acquisition equipment
    Put all workpieces and samples in your project box. Anything left at the equipment will be disposed of
    Coat any steel surfaces in oil, to prevent corrosion, where applicable

## Slide 33: Working in the MMRI – Machine Shop and Waterjet Room
Machinery and Training
  The Machine Shop contains a range of high powered and potentially lethal equipment
  Do not operate equipment within the machine shop that you have not been trained to use
    Discuss training needs with one of the staff or your supervisor. Observing a student operating a piece of equipment does not replace proper training
  If it has been a while since you used a machine or piece of equipment, do not be afraid to ask one of the staff to provide you with a refresher
  If you have any doubts or concerns about your setup or process, review it with one of the staff members
When welding, grinding, or performing other activities that generate fumes or odors, use the snorkel built into the room. Make sure that it is working by listening to it as it starts up

## Slide 34: Working in the MMRI – MPAL
Machinery and Training
  MPAL contains a range of sensitive equipment, all of which have moving components. Therefore, please keep loose clothing and hands away from any moving parts
  Do not operate equipment that you have not received training for. Discuss training needs with one of the staff or your supervisor
  Do not make any attachment changes without first consulting the staff in charge
  Do not provide training to others unless you have been designated to do so by a supervisor
  If it has been a while since you last used a piece of equipment, do not hesitate to ask one of the staff members in charge for a refresher or even a complete training session
  If you have any doubts or concerns about your setup or process, review them with one of the designated staff members. Next to each piece of equipment, you can find the SOP. Always adhere to these SOPs

## Slide 35: Working in the MMRI – Coater Lab
Machinery and Training
  The coater is equipped with a variety of high-powered connections, so caution is essential when working around them
  Do not attempt to operate the coater or touch any of its components unless you have received proper training and/or have been assigned by a supervisor
  Exercise caution around hot surfaces after deposition and when the chamber is open
  When closing the door, be mindful of the vacuum suction to avoid any hand-related incidents
  Do not handle the gas cylinders unless you have obtained proper training and permission from a supervisor. Operate with care and adhere to appropriate safety procedures
  The snorkel should be in use while a deposition cycle is in progress

## Slide 36: Working in the MMRI – MPAL and Coater Lab
Chemical Handling
  Only chemicals like Acetone, Isopropanol, and Ethanol are permitted for use in MPAL and the Coater lab
  Ask the staff in charge before using any chemical
  Carefully handle the chemicals to avoid spills, and use gloves
  Make sure not to inhale or expose cuts to the chemicals
  Proper disposal containers must be used. Ask the staff in charge before disposing of any chemical if you are not sure about the proper chemical disposal procedure